## Slide 1: Communications and Radar-Supported Transportation Operations and Planning (CAR-STOP)
Project 0-6877
TxDOT PM: Darrin Jensen
Research Supervisor: Chandra Bhat
Researchers: Joydeep Ghosh, Robert Heath, Junil Choi, Mohammed Eltayeb
  Graduate RAs: Taewan Kim, Michael Motro, Rahi Kalantari, Preeti Kumari, Enoch Yeh, Anum Ali, Alice Chu, Subodh Dubey

## Slide 2: Outline
Project motivation
Work description in detail
Q&A

## Slide 3
Motivation

## Slide 4: Project motivation
CRASHES  Enormous cost to society
2,310,000
2013 injuries in US*
232,041
Injuries in TX
32,719
2013 death in US**
3,382
Death in TX
*: NHTSA, 2014
**: TxDOT, 2014
Property damage
Productivity loss
Injury
Death
Cost almost $1 trillion!!!

## Slide 5: CAR-STOP approach
Multidisciplinary approach to improve CA/CW
1
2
3
TRANSPORTATION
WIRELESS
MACHINE
LEARNING
Communication
and radar
technologies
Distributed
decision
making
Transportation aspects

## Slide 6: UT expertise for CAR-STOP
Wireless communication
MmWave & V2X communications
Radar signal processing
Prototyping
Machine learning & BigDATA
Dynamic vehicular environment
modeling
Driver psychology modeling
Driver habitats modeling
Smart transportation
Chandra Bhat
Robert W. Heath
Joydeep Ghosh
Distributed decision making

## Slide 7: CAR-STOP at a glance
Which prior info?
How do we obtain info?
How do we use info?
IMPROVED
SAFETY
Exploit prior info
Driver´s behavior
Typical traffic condition
Joint radar and communications
Waveform / hardware / antenna design
Security needed to prevent spoofing
Collision warning/avoidance algorithms
Smart combination of information
Distributed decision making
SAFE

## Slide 8: Project scope
Developing Joint Automotive Radar and Communication at the mmWave Band
Conceptual and Functional Framework for Integrating Communications and Radar
Task 1
Task 2
Conduct Preliminary Tests
and Develop Concept of Operations (CONOPS)
Task 3
Complete research plan for full development

## Slide 9
Contributions Task 1

## Slide 10: Task 1: Definition and contributions
Conceptual and functional framework for integrating communications and radar
TASK 1
CONTRIBUTIONS
□ Improve trajectory prediction from prior information
  Utilizes motion pattern
□ Evaluate CW capability using DSRC and simple warning system
  Incorporates driver behavior & vehicular dynamics
1.1. Improved CW/CA for cars
Months 1-10
1.2 Improved CW/CA for pedestrians and bicycles
Months 7-13
1.3. Dealing with uncertainty
Months 7-13

## Slide 11: Subtask 1.1: Develop improved collision detection and avoidance algorithms for cars
- Vehicle CW/CA System
Future Trajectory Prediction
Detect Potential Trajectory Conflict
Collision Warning (CW)
Collision Avoidance (CA)
Current State Estimation
Workpackage 1.1.1: Combining information from the communication and radar systems
Workpackage 1.1.2: Incorporating vehicular dynamics and driver behavior

## Slide 12: Data Acquisition
NGSIM

## Slide 13: Vehicular ad-hoc network (VANET) simulations of overtaking maneuvers on two-lane rural highways (1.1.1)
DSRC Communication
Range far enough to be reliable?
Can send enough information?
Noise in information?
Driver behavior
how fast to accelerate
How close to passed car
100mW
Normal DSRC protocol
  Overtaking warning system: alerts driver if overtaking maneuver is unsafe
Chart: Accuracy of Overtaking Warning System
| 0.0 | 0.5 | 0.75 | 1.0
Missed Warnings | 0.112 | 0.066 | 0.029 | 0
False Warnings | 0.119 | 0.097 | 0.058 | 0.004
Knowledge of driver behavior

## Slide 14: Difficulty of future trajectory prediction
Utilize further information for better prediction
Motion Pattern: possible behavior of vehicle
Hole
Crack
w/o Motion Pattern
Most vehicles’ trajectory
Vehicle direction
Current position
Notes: Example. Suppose there has been a hole in a road for a while.
Without any further information, trajectory prediction algorithm will give smooth curve for turning left.
However, most vehicles detour around the whole with unexpected curve.

## Slide 15: Motion pattern clustering and classification
Different techniques used to cluster (group) the trajectories - EM (Expectation Maximization) - DTW(Dynamic Time Warping) - Map Based

## Slide 16: Physics-based Trajectory Prediction

## Slide 17: Learning-based Trajectory Prediction

## Slide 18: Future plans for trajectory prediction
Smart motion pattern/physics fusion
Gaussian process
Road–Motion connection
Many atypical roads – can’t get data for every road
Connect road characteristics to driver actions

## Slide 19: Future plans for collision avoidance
Warning
Takeover
Autonomous
Questions:
Can DSRC provide enough info to prevent collisions? (1.3.2)
mmWave?
Can pedestrians/cyclists be dealt with the same way? (1.2.1)
What about other autonomous cars? (1.3.3)

## Slide 20
Contributions Task 2

## Slide 21: Task 2: Definition and contributions
Joint automotive radar and communication at the mmWave band
TASK 2
2.1. Develop a framework for joint mmWave communications and radar
2.2. Optimizing the Joint Waveform to Meet Different Objectives
CONTRIBUTIONS
      □ Make mmWave work for vehicles
      □ Demonstrate radar using low frequency WiFi signals
      □ Study joint communication and radar systems at mmWave
Months 1-10
Months 7-13
2.2. Incorporating Antenna Arrays
Months 7-13
2.2. Dealing with security issues
Months 7-13

## Slide 22: Background on radar and vehicular communications
MmWave radars widely used in automotive safety applications
  Expensive: automotive radar modules cost around $1,500
  Easy to get spoofed compared to communication
Current V2X communications are based on WLAN standards
  Safety applications possible: Forward collision warning, do not pass warning …
  Maximum data rate of 27 Mbps
Communication or radar alone not enough for safety applications
Long range
radar beam
Target Vehicle
Estimate range and
velocity from reflected signal
Long, medium and short range radar with different applications
Vehicle to infrastructure
(V2I)
communication
Vehicle to vehicle (V2V)
communication

## Slide 23: Motivation for joint radar and communications at mmWave
MmWave radio frequency spectrums are
  Already adopted in automotive radar
  Know-how exists among automotive suppliers
  Already employed in latest WLAN applications
  Low cost device production
Joint mmWave communication and radar systems
  May build on existing mmWave wireless communication standards
  Low cost / higher data rates / secure / increase penetration rate
30 GHz
300 GHz
60 GHz
unlicensed
70-90 GHz
Automotive radar (76-81 GHz)
Automotive radar (24/26 GHz)
38-49 GHz
28 GHz
possible 5G cellular bands
unlicensed spectrum
automotive radar

## Slide 24: Fundamentals on mmWave communication
MmWave communication is different
  Severe signal attenuation / sensitivity to blockages
  Large antenna arrays
  Directional beamforming
Large bandwidth enables high data rates and high accuracy for radar
Knowledge on mmWave communication will guide joint radar & comm.
directional beamforming
blockage
mmWave
base station
V2I communication
beam
V2V communication beam

## Slide 25: Making mmWave work for vehicles
Choosing the beamwidth in joint radar-communication mmWave systems
  Account for mobility and beam pointing error*
Optimum beam is “pointy” but not too narrow
*V. Va and R. W. Heath Jr., “Basic relationship between channel coherence time and beamwidth in vehicular channels,” to appear in VTC-Fall, Sept. 2015.
A
B
different beam widths
beam pointing error

## Slide 26: Radar testbed using low-frequency WLAN signals
Figure 2: Map and picture of measurement location in vacant parking lot. Vehicle used during testing was a 2002 Toyota Camry.
Real-time implementation and fields tests
  Leverage existing National Instruments hardware
  Exploit sub-mmWave WLAN signals as a proof-of-concept for mmWave
Show that it is possible to use a communication signal for ranging
  Sub-meter accuracy achieved in single target setting
  More advanced algorithms under study to improve performance
Comm.-RADAR
link setup
2002 Toyota Camry
Location of
measurements
Alternative radar solution with lower cost

## Slide 27: Initial framework for mmWave joint communication and radar
Build from the recently released consumer mmWave WLAN standard
  Motivates a common radar and communication standard at the mmWave band
  Lower cost since WLAN chips are cheap and high volume
Developed mmWave WLAN framework works well as a long range radar*
  Leverages WLAN receiver algorithms for radar parameter estimation
  Achieved desired accuracy for range and velocity estimation
* Preeti Kumari, Nuria González Prelcic and Robert W. Heath, Jr, “Investigating the IEEE 802.11ad Standard for Millimeter Wave Automotive Radar,” to appear in VTC-Fall, Sept. 2015.

## Slide 28: Subtask 2.1: Future Plans
Joint mmWave radar and communication
  Study trade-off between radar and communication using mmWave WLAN standard
  Optimize the framework for better radar performance
Making mmWave work for vehicles
  Understand the overhead of beam alignment
  Exploit radar/DSRC to reduce beam alignment overhead
  Incorporate these results to radar performance evaluation
Demonstrate radar using low-frequency WLAN signals
  Conduct a head-to-head comparison with mmWave radar

## Slide 29: Subtask 2.2: Optimizing the Joint Waveform
FUTURE PLANS
  Define different working scenarios
    Bicycle near a car / several cars ahead, avoid collision with pedestrian, etc.
FUTURE PLANS
Design optimization strategies
  Define cost functions and constraints
  Optimize radar and communication parameters depending on scenarios
Adapt waveform with environmental situation
  Rural / urban area
  Vehicle / communication traffic
Waveform design is related to limited resources
  Bandwidth, power, time

## Slide 30: Subtask 2.3: Incorporating antenna arrays
FUTURE PLANS
Design antenna architecture for joint radar & comm.
  Investigate a unified architecture for radar and comm.
Antenna arrays are important to
  Radar systems
  MmWave communication systems
FUTURE PLANS
Design beamforming algorithm for joint radar & comm.
    Radar with hybrid beamforming never explored before
Performance metric for radar and communication may conflict
  COMM: Maximize receive power
  RADAR: Better target detection

## Slide 31: Subtask 2.4: Dealing with security issues
FUTURE PLANS
Physical layer security with large antenna arrays
  MmWave with large number of antennas may allow additional security
  Using antenna subsets to prevent eavesdropping
Connected vehicles vulnerable to cyber attacks
Recent demonstration on Jeep hacking
Lack of privacy on connected vehicles may lead to “Big Brother”
FUTURE PLANS
Analysis of security in automotive case
  Study the fundamental limit of security using subsets
  Study the impact of secured beamforming on radar
Current security/privacy protocols based on digital signature
Large number of digital key pairs should be changed often
Digital key can be breached

## Slide 32
Future Plans Task 3

## Slide 33: Task 3: Definition and work plan
Conduct Preliminary Tests and Develop Concept of Operations
TASK 3
3.1. Preliminary tests with real data
3.2. Asses benefits of proposed system and develop CONOPS
FUTURE PLANS
      □ Collect real data with prototyping
      □ Optimize developed algorithms/systems with real data
Months 8-13
Months 9-15
FUTURE PLANS
      □ Asses benefits of proposed system
      □ Develop CONOPS

## Slide 34: Prototyping plan
L-COM 23-dBi HG4958-23P Patch
- 2 receive (RX)
- 1 transmit (TX)
TX
RX
RX
Delphi ESR 2.5 77 GHz RADAR
National Instruments
USRP-RIO w/ 5.8 GHz
RF, 802.11p PHY+MAC
National Instruments
PXI Chassis Interfaces with USRP-RIO & ESR
Test using IEEE 802.11p
Redundant radar
Target information sharing
ESR forward target cross-checking for validation
Collect real data with prototyping (3.1.1)
Optimize developed algorithms/systems with real data (3.1.2)

## Slide 35: Subtask 3.1 Environments to Consider (in and around UT Austin)
Where
  Traffic Volume of Road User Mix: Cars, Heavy Vehicles/Buses, Motorcycles, Pedestrians, Bicyclists
  Routes: Intersections (Four-Way, T, Y, Traffic Circle, Atypical), Non-Intersections, Construction Sites
  Interactions with Non-Connected Vehicles
  High-Incident Areas: Focus on Frontal Collision Scenarios
  Roadway Alignment: Straight, Curved (Curve Radius: ≥ 500, ≥ 250, ≥ 125)
  Speed Limits: < 20mph, 20-45 mph, 45-60 mph, > 60 mph

## Slide 36: Subtask 3.1 Environments to Consider (in and around UT Austin)
When
  Day of Week: Weekday, Weekend
  Time of Day: AM Off-Peak, AM Peak, PM Off-Peak, PM Peak, Evening
  Weather Conditions: Clear, Cloudy, Rainy

## Slide 37: Subtask 3.1 Environments to Consider (in and around UT Austin)
How
  Communication Technology to Consider: DSRC, mmWave Communication
  Sensing Technology to Consider: Radar (LRR, SRR), Lidar, GPS, Cameras, Ultrasound
  Data to Collect: Accuracy and resolution of measured parameters for sensing, probability of detection and false alarm rate for sensing, bit error rate and throughput for communication, range of operation

## Slide 38: Thank You
Questions, Comments or Suggestions?